## Slide 1: Lab 2 Energy efficient image processing

## Slide 2: Objective and organization
Demonstrates how manipulation of an image can be used to tradeoff image quality to save power in emissive displays
  1 report – 2 days
  Matlab
Organize all implemented methods in functions and scripts to automatically test and evaluate all images and all techniques

## Slide 3: OLED vs LED
OLED TVs
  Do not require external lighting
    Better black levels

## Slide 4: OLED vs LED
OLED TVs
  Pixels are independent from each other
    More sense of depth
    Higher contrast makes images more realistic

## Slide 5: OLED
Interesting case study from our perspective…
Organic light-emitting diode (OLED)
  Do not require external lighting
  Pixels are emissive
    Emissive layer is a film of organic compound which emits light in response to an electric current
  Each pixel is made of three devices corresponding to red, green and blue components

## Slide 6
In LCDs, backlight dominates power consumption and color has only negligible power impact
With OLED displays, the color of a pixel impacts on power consumption
  E.g., hungry blue
  Different luminance efficacies
  Different images imply different power consumption
OLED

## Slide 7: OLED
Power consumption depends on color components of a pixel…
  So we can save power by changing the spectrum of the image!
  First class of power saving methods:
    Change pixel color
    Given a certain tolerance level on color distorsion

## Slide 8
Compute power consumption
Apply image transformation
Compute distortion
Compute power consumption
Evaluate the power consumption / image distortion tradeoff

## Slide 9
Assignment 1

## Slide 10
Compute power consumption
Apply RGB-base distortions
Compute distortion
Compute power consumption
Evaluate the power consumption / image distortion tradeoff

## Slide 11: 1. Identification of images
Test images will be:
  10 color images from the USC SIPI database
    http://sipi.usc.edu/database/database.php?volume=misc
  5 images representing different screenshots of your computer
Different colors and characteristics…

## Slide 12: 2. Manipulation of images
Experiments require to adopt different color spaces…
TASK: Learn how to:
  Import the image
    imread() function
  Extract the R, G, B channels
  Convert between different color spaces
Refer to:
  http://it.mathworks.com/help/images/index.html

## Slide 14: 2. Manipulation of images
RGB
  Additive color space
    All possible colors that can be made from three colorants for red, green and blue
  Stores individual values for red, green and blue
  Convenient color model for computer graphics as it is similar to the human visual system
    Used in LCDs

## Slide 15: 2. Manipulation of images
Lab
  One channel for luminance (L) and two color channels (a and b)
  Includes all perceivable colors
    Super-set of RGB
  The space is a three-dimensional Real number space
    Allows the definition of Euclidean distance

## Slide 16: 2. Manipulation of images
HSV
  Hue
    Perceived color
  Saturation
    Colorfulness, amount of white component
  Value
    Brightness
  Cylindrical-coordinate representations of points in an RGB color model
  Widely used in computer graphics

## Slide 17
Compute power consumption
Apply RGB-base distortions
Compute distortion
Compute power consumption
Evaluate the power consumption / image distortion tradeoff

## Slide 18: 3. Evaluation of power consumption
Power model
    Depends on pixel color in terms of RGB components
    f, h and k determined experimentally by:
      Setting black screen to estimate C
      For f, set G and B components to 0 and vary R component
      Similar for h and k
    Sums up power contributions of single pixels
    C static power independent of pixel values

## Slide 19: 1. Evaluation of power consumption
Experimental Setup:
  Show monochromatic images with different RGB values on the OLED, e.g.:
  Measure power supply current (and convert to power)

## Slide 20: 1. Power model for the provided OLED (cont’d)
Interpolation:
  Find regression model type that fits best the data and determine the corresponding parameters
  For this Lab, we used a model format from literature (see next slide)

## Slide 21: 3. Evaluation of power consumption
TASK: Define a MATLAB function that estimates power consumed to display an image
  R, G, B are pixel values between 0 and 255
γ | W0 | WR | WG | WB
0.7755 | 1.48169521*10-6 | 2.13636845*10-7 | 1.77746705*10-7 | 2.14348309*10-7

## Slide 22
Compute power consumption
Apply RGB-base distortions
Compute distortion
Compute power consumption
Evaluate the power consumption / image distortion tradeoff

## Slide 23: 4. Evaluation of image distortion
Transformations imply a distorsion
  Perceived by the eye (not a scientific measure!)
  Must determine a measure of distortion based on the distance between images…
Work in the L*a*b* space
Has a notion of Euclidean distance between colors
Can define what is the distance between two images..

## Slide 24: 4. Evaluation of image distortion
Evaluation of image distortion
  Difference between two images
    N = number of pixels
    k = kth bit
    Bit per bit, compute the difference of L, a and b components between the two images

## Slide 25: 4. Evaluation of image distortion
TASK: Define a MATLAB function that estimated the distortion w.r.t. the original image
  Work in the L*a*b* space and compute the Euclidian distance pixel per pixel
  Convert by using MATLAB’s rgb2lab() and lab2rgb() functions

## Slide 26: 4. Evaluation of image distortion
Think also in terms of percentage distortion
  E.g., distortion of new image w.r.t. distortion between a black and a white image

## Slide 27: 4. Evaluation of image distortion (cont’d)
Alternative: Mean Structural Similarity Index (MSSIM).
  More complex metric involving measures of brightness, contrast and structural distortion
  Implementation provided by MATLAB: ssim(A, B)
  Score between 0 and 1 (1 = identical images).
    Convert to % simply by multiplying * 100
TASK: Compare the two distortion metrics and determine which one correlates better with visual differences

## Slide 28
Compute power consumption
Apply RGB-base distortions
Compute distortion
Compute power consumption
Evaluate the power consumption / image distortion tradeoff

## Slide 29: 5. Evaluation of various strategies on image modification
TASK: Experiment image manipulation strategies to reduce power consumption:
  Pixel-wise transformations
    Work on colors
  Histogram equalization
    Work on luminance
  Other types of brightness/contrast modifications
Apply to all images

## Slide 30: 5. Evaluation of various strategies on image modification
Hungry-blue:
  Blue is the more costly component..
  So, subtract a constant value to the blue component
  Will introduce a distortion but reduces power
    Depending on the weight of the blue component
Histogram equalization:
  Flatten the histogram of the image, e.g., by working on luminance…
  Requires to work in the HSV color space
    Hue – saturation – value (i.e., luminance)
  Introduces distortion
Other types of brightness/contrast transformations:
  E.g. Convert to HSV and scale the value component (V  k*V with k < 1) or do some more complex transformation
  use your imagination

## Slide 31
Compute power consumption
Apply RGB-base distortions
Compute distortion
Compute power consumption
Evaluate the power consumption / image distortion tradeoff

## Slide 32: 6. Analysis
Analyse power/distortion tradeoff
  Do different images behave differently?
  What changes in terms of power consumption with different manipulation strategies?
  How can I save more power with lower distorsions?
  …
TASK: Compare the transformations you applied and find the solution that minimizes power consumption under a maximum average distortion constraint (1%, 5%, 10%)
  Use both distortion metrics

## Slide 33: 6. Analysis
Example:
  Blue reduction
    Power saving 29.11%
    Distortion 30.99%
  Histogram equalization
    Power saving 11.99%
    Distortion 8.46%

## Slide 34: How to:
Learn how to load an image in MATLAB
  And how to convert it to RGB
Write the function to estimate power consumption
Write the function to estimate distortion