## Slide 1: Lab 2 Energy efficient image processing

## Slide 2: Objective and organization
Demonstrates how manipulation of an image can be used to tradeoff image quality to save power in emissive displays
  1 report – 2 days
  Matlab + C (Arduino)
Organize all implemented methods in functions and scripts to automatically test and evaluate all images and all techniques

## Slide 3
Assignment 2

## Slide 4: Objective
Test the pixel transformations studied in the first session on a real compact OLED display.
  Check the real visual quality of the output on the screen.

## Slide 5
Compute power consumption
1

## Slide 6
Send image to the OLED through the embedded board
Compute power consumption
1
2

## Slide 7
Compute power consumption
Apply image transformations (in MATLAB)
1
2
3
Send image to the OLED through the embedded board

## Slide 8
Send image to the OLED through the embedded board
Compute power consumption
Apply image transformations (in MATLAB)
1
2
Compute distortion
Compute power consumption
3
4

## Slide 9
Send image to the OLED through the embedded board
Compute power consumption
Apply image transformations (in MATLAB)
1
2
Compute distortion
Compute power consumption
3
4
5

## Slide 10
Send image to the OLED through the embedded board
Compute power consumption
Apply image transformations (in MATLAB)
1
2
Compute distortion
Compute power consumption
3
4
Evaluate the power consumption / image distortion tradeoff
5

## Slide 11
Send image to the OLED through the embedded board
Compute power consumption
Apply image transformations (in MATLAB)
1
2
Compute distortion
Compute power consumption
3
4
Apply image transformations in the board’s MCU
6
Evaluate the power consumption / image distortion tradeoff
5

## Slide 12
Assignment 2: how to

## Slide 13
Send image to the OLED through the embedded board
Compute power consumption
Apply image transformations (in MATLAB)
1
2
Compute distortion
Compute power consumption
3
4
Apply image transformations in the board’s MCU
6
Evaluate the power consumption / image distortion tradeoff
5

## Slide 14: 2. Send image to the OLED
Provided setup:
  Arduino Uno board (https://store.arduino.cc/arduino-uno-rev3)
  128x128 New Haven Display NHD-1.5-128128ASC3 (https://eu.mouser.com/datasheet/2/291/NHD-1.5-128128ASC3-784468.pdf)
  USB cable (??)
  GPIO connection cables

## Slide 15: 2. Send image to the OLED
Communication mechanisms:
  The OLED receives configurations and pixel data through an SPI interface (implemented through the Arduino GPIOs)
  For sending images from the PC to the Arduino, we use RS-232 over USB
  IMPORTANT: The Arduino Uno’s MCU does not have enough memory to store the entire 128x128 image (128x128x3 bytes required). So, pixels must be immediately forwarded from the RS-232 bus to the SPI bus.

## Slide 16: 2. Send image to the OLED
Arduino/OLED connection:
Writing firmware for Arduino Uno:
  Done using the Arduino IDE (https://www.arduino.cc/en/main/software)
  Simplified C/C++ dialect
PIN Function | SCK | MOSI | NRST | Chip Select | Data/Control | VDD | GND
Arduino Name | D13 | D11 | D6 | D5 | D4 | 3.3V | GND
OLED Name | SCK | MOSI | /RES | OLEDCS | D/C | VDD | GND

## Slide 17: 2. Send image to the OLED
MATLAB code to implement:
  Read an image (imread)
  Resize it to fit the display (imresizse)
  Convert it to the appropriate color representation
    The provided OLED uses 18-bit RGB (6-bit per color channel)
    It also expects data in B-G-R order (vs. R-G-B)
  Send pixels to the Arduino through RS-232
    Using MATLAB’s serial I/O functionalities
    serial(), fopen(), frwrite(), flushoutput(), fclose()

## Slide 18: 2. Send image to the OLED
MATLAB code to implement (cont’d):
  To make the communication more reliable, add a mechanism to signal the beginning of a new image to the Arduino
    Useful in case of interrupted communication
    Exploit the 6-bit per channel color representation (the 2 MSBs of each byte sent on the RS-232 are unused, and typically will be 0s).
    Send a special byte with those 2 bits at 1 at the beginning to signal the start of a new image.

## Slide 19: 2. Send image to the OLED
MATLAB code to implement (cont’d):
  Set the RS-232 Baud Rate in MATLAB (and Arduino) to a value <= 115200 to avoid data losses.
  Opening the RS-232 file on the PC resets the Arduino.
    Add a «wait» of few seconds before starting to send data
    Also wait some time between the first «start» byte and the rest of the data, to allow the OLED to reconfigure itself.

## Slide 20: 2. Send image to the OLED
Arduino code provided:
  Basic OLED functions (initialize, setup, send pixel, etc.)
Arduino code to implement:
  Initialize OLED and communication interfaces at boot time
  Forward pixel values received on the RS-232 to the OLED
    Reset OLED address when a «start» byte is received

## Slide 21: 2. Send image to the OLED
Arduino code to implement (cont’d):
  Initialize OLED and communication interfaces at boot time
    OLED_setup(): setup pins used by the Arduino/OLED interface, configure Serial (RS232) and SPI interfaces
    OLED_init(): initialize OLED display with default settings

## Slide 22: 2. Send image to the OLED
Arduino code to implement (cont’d):
  Forward pixel values received on the RS-232 to the OLED
    void serialEvent(): default ISR to handle RS232 events (received bytes)
    Serial.read(): read one char from the RS232 channel (cast output to uint8_t).
    Serial.available(): check if there are bytes available for reading in the RS232 channel

## Slide 23: 2. Send image to the OLED
Arduino code to implement (cont’d):
  Forward pixel values received on the RS-232 to the OLED
    OLED_Data_128128RGB(): write the next color component to the screen
      Pixel addresses are updated automatically.
      Remember the BGR color order
    OLED_SetRowAddress_128128RGB() and OLED_SetColumnAddress_128128RGB(): set the starting address for a new image
    OLED_WriteMemoryStart_128128RGB(): enable writing to the OLED’s internal memory

## Slide 24
Send image to the OLED through the embedded board
Compute power consumption
Apply image transformations (in MATLAB)
1
2
Compute distortion
Compute power consumption
3
4
Apply image transformations in the board’s MCU
6
Evaluate the power consumption / image distortion tradeoff
5

## Slide 25: 3. Apply image transformations
Same as Session 1:
  Apply pixel-level transformations (blue reduction, pixel value scaling, cubic transformation, etc.)
  Apply these transformations before processing the image for transmission

## Slide 26
Send image to the OLED through the embedded board
Compute power consumption
Apply image transformations (in MATLAB)
1
2
Compute distortion
Compute power consumption
3
4
Apply image transformations in the board’s MCU
6
Evaluate the power consumption / image distortion tradeoff
5

## Slide 27: 4. Compute distortion and evaluate trade-off
Almost the same as Session 1
Small difference:
  Some «distortions» are eliminated when converting to 6-bit RGB and resizing the image

## Slide 28
Send image to the OLED through the embedded board
Compute power consumption
Apply image transformations (in MATLAB)
1
2
Compute distortion
Compute power consumption
3
4
Apply image transformations in the board’s MCU
6
Evaluate the power consumption / image distortion tradeoff
5

## Slide 29: 6. Apply image transformations in the board
What kind of transformations can be applied?
What are the differences compared to MATLAB?